## Slide 1
Lab and Deployable VPX Chassis Solution for
19“ Cabinets and Bench Top Applications
For development, testing and final deployment of VPX Conduction Cooled or Airflow Through modules Pluggable to standard VPX 3U slots,
COMTEL Electronics GmbH, Phone: +49 89 43 77 89 –0,
Sales: sales@comtel-online.com Web: www.comtel-online.com
VPX S-Frame - 19" 5U 8 Slot System
PRODUCT DATASHEET
Rugged Sheet Metal Enclosure
For use in 19" Racks or Bench Top with Front to Rear Air Cooling
Interchangeable individual Front Card Slots for:
  3U Conduction Cooled ANSI/VITA 48.2
  Air-cooled Plug-in Modules ANSI/VITA 48.1
  Air Flow Through AFT Plug-In Modules ANSI/VITA 48.5.
Or
  Any combination
RTM Card access
Integrated 1500W AC PSU with IEC-320 C14 AC Power Entry
Backplane with Comtel’s high-speed technology for 25Gbps per differential pair is available
Front Panel with Touchscreen display
AFT
Configuration
Air-/-Plane®

## Slide 2
Features
Integrated Backplane:
  VITA 46 Compliant
  8x 3U Slots with 2" Slot pitch
  Comtel’s high-speed Air-/Plane® technology for 25Gbps per differential pair is available
Integrated Power Supply:
  Input Voltage: 90-264 VAC
  Frequency: 47 – 63 Hz
  Input Current
    8A for 114VAC, (TBA)
    4A for 230 VAC (TBA)
  Max. Inrush Current
    65A for 114VAC, (TBA)
    125A for 230 VAC (TBA)
Power:
  Up to 150W per Slot at 25°C ambient
Air Cooling:
  Front to Rear
  Max. Air Flow: TBA
  Noise: TBA
Dimensions (mm):
  Width 482.6
  Height 222.0 (5U)
  Length 270.0 (310.0 with handles)
  2” pitch card frame
Environment (default):
  Operating temperature 0 to +50°C
  Relative Humidity Non-condensing 20-80%
  Operation Altitude：5000m
VPX S-Frame - 19" 5U 8 Slot System
PRODUCT DATASHEET
Conduction Cooled
Configuration
Rear view
RTM access